## Slide 1: Computer Organization and Architecture Designing for Performance
11th Edition, Global Edition
Chapter 19
Control Unit Operation and Microprogrammed Control

## Slide 2: Micro-Operations
The functional, or atomic, operations of a processor
Series of steps, each of which involves the processor registers
Micro refers to the fact that each step is very simple and accomplishes very little
The execution of a program consists of the sequential execution of instructions
  Each instruction is executed during an instruction cycle made up of shorter subcycles (fetch, indirect, execute, interrupt)
  The execution of each subcycle involves one or more shorter operations (micro-operations)
Notes: We have seen that the operation of a computer, in executing a program, consists of a
sequence of instruction cycles, with one machine instruction per cycle. Of course, we
must remember that this sequence of instruction cycles is not necessarily the same
as the written sequence of instructions that make up the program, because of the
existence of branching instructions. What we are referring to here is the execution
time sequence of instructions.
We have further seen that each instruction cycle is made up of a number of
smaller units. One subdivision that we found convenient is fetch, indirect, execute,
and interrupt, with only fetch and execute cycles always occurring.
To design a control unit, however, we need to break down the description
further. In our discussion of pipelining in Chapter 16, we began to see that a further
decomposition is possible. In fact, we will see that each of the smaller cycles
involves a series of steps, each of which involves the processor registers. We will
refer to these steps as micro-operations. The prefix micro refers to the fact that each
step is very simple and accomplishes very little,
Micro-operations are the functional, or atomic, operations of a processor. In this
section, we will examine micro-operations to gain an understanding of how the events
of any instruction cycle can be described as a sequence of such micro-operations.
A simple example will be used. In the remainder of this chapter, we then show how the
concept of micro-operations serves as a guide to the design of the control unit.

## Slide 3: Figure 19.1 Constituent Elements of a Program Execution
Notes: Figure 19.1 depicts the relationship
among the various concepts we have been discussing. To summarize, the execution
of a program consists of the sequential execution of instructions. Each instruction
is executed during an instruction cycle made up of shorter subcycles (e.g., fetch,
indirect, execute, interrupt). The execution of each subcycle involves one or more
shorter operations, that is, micro-operations.

## Slide 4: The Fetch Cycle
Occurs at the beginning of each instruction cycle and causes an instruction to be fetched from memory
Four registers are involved:
  Memory Address Register (MAR)
    Connected to address bus
    Specifies address for read or write operation
  Memory Buffer Register (MBR)
    Connected to data bus
    Holds data to write or last data read
  Program Counter (PC)
    Holds address of next instruction to be fetched
  Instruction Register (IR)
    Holds last instruction fetched
Notes: We begin by looking at the fetch cycle, which occurs at the beginning of each instruction
cycle and causes an instruction to be fetched from memory. For purposes of
discussion, we assume the organization depicted in Figure 16.5 (Data Flow, Fetch
Cycle). Four registers are involved:
■ Memory address register (MAR): Is connected to the address lines of the system
bus. It specifies the address in memory for a read or write operation.
■ Memory buffer register (MBR): Is connected to the data lines of the system bus.
It contains the value to be stored in memory or the last value read from memory.
■ Program counter (PC): Holds the address of the next instruction to be
fetched.
■ Instruction register (IR): Holds the last instruction fetched.

## Slide 5: Figure 19.2 Sequence of Events, Fetch Cycle
Notes: Let us look at the sequence of events for the fetch cycle from the point of view
of its effect on the processor registers. An example appears in Figure 19.2. At the
beginning of the fetch cycle, the address of the next instruction to be executed is in
the program counter (PC); in this case, the address is 1100100. The first step is to
move that address to the memory address register (MAR) because this is the only
register connected to the address lines of the system bus. The second step is to bring
in the instruction. The desired address (in the MAR) is placed on the address bus,
the control unit issues a READ command on the control bus, and the result appears
on the data bus and is copied into the memory buffer register (MBR). We also need
to increment the PC by the instruction length to get ready for the next instruction.
Because these two actions (read word from memory, increment PC) do not interfere
with each other, we can do them simultaneously to save time. The third step is
to move the contents of the MBR to the instruction register (IR). This frees up the
MBR for use during a possible indirect cycle.
Thus, the simple fetch cycle actually consists of three steps and four micro-operations.
Each micro-operation involves the movement of data into or out of a
register. So long as these movements do not interfere with one another, several of
them can take place during one step, saving time.

## Slide 6: Rules for Micro-Operations Grouping
Proper sequence must be followed
  MAR  (PC) must precede MBR  (memory)
Conflicts must be avoided
  Must not read and write same register at same time
  MBR  (memory) and IR  (MBR) must not be in same cycle
One of the micro-operations involves an addition
  To avoid duplication of circuitry, this addition could be performed by the ALU
  The use of the ALU may involve additional micro-operations, depending on the functionality of the ALU and the organization of the processor
Notes: The groupings of micro-operations must follow two simple rules:
1. The proper sequence of events must be followed. Thus (MAR  (PC)) must
precede (MBR  Memory) because the memory read operation makes use of
the address in the MAR.
2. Conflicts must be avoided. One should not attempt to read to and write from
the same register in one time unit, because the results would be unpredictable.
For example, the micro-operations (MBR  Memory) and (IR  MBR)
should not occur during the same time unit.
A final point worth noting is that one of the micro-operations
involves an addition. To avoid duplication of circuitry, this addition could be performed by
the ALU. The use of the ALU may involve additional micro-operations,
depending on the functionality of the ALU and the organization of the processor. We defer a
discussion of this point until later in this chapter.
It is useful to compare events described in this and the following subsections to
Figure 3.5 (Example of Program Execution ). Whereas micro-operations
are ignored in that figure, this discussion shows the micro-operations
needed to perform the subcycles of the instruction cycle.

## Slide 7: Indirect Cycle
Once an instruction is fetched, the next step is to fetch source operands
Assuming a one-address instruction format, with direct and indirect addressing allowed:
  If the instruction specifies an indirect address, then an indirect cycle must precede the execute cycle
  The address field of the instruction is transferred to the MAR
  This is then used to fetch the address of the operand
  Finally, the address field of the IR is updated from the MBR, so that it now contains a direct rather than an indirect address
  The IR is now in the same state as if indirect addressing had not been used, and it is ready for the execute cycle
Notes: Once an instruction is fetched, the next step is to fetch source operands. Continuing our
simple example, let us assume a one-address instruction format, with direct and indirect
addressing allowed. If the instruction specifies an indirect address, then an indirect cycle
must precede the execute cycle. The data flow differs somewhat from that indicated in
Figure 16.6 (Data Flow, Indirect Cycle) and includes the following micro-operations:
t1: MAR  (IR(Address))
t2: MBR  Memory
t3: IR(Address)  (MBR(Address))
The address field of the instruction is transferred to the MAR. This is then used
to fetch the address of the operand. Finally, the address field of the IR is updated
from the MBR, so that it now contains a direct rather than an indirect address.
The IR is now in the same state as if indirect addressing had not been used,
and it is ready for the execute cycle. We skip that cycle for a moment, to consider
the interrupt cycle.

## Slide 8: Interrupt Cycle
At the completion of the execute cycle, a test is made to determine whether any enabled interrupts have occurred, and if so, the interrupt cycle occurs
The nature of this cycle varies greatly from one machine to another
In a simple sequence of events:
  In the first step the contents of the PC are transferred to the MBR so that they can be saved for return from the interrupt
  Then the MAR is loaded with the address at which the contents of the PC are to be saved, and the PC is loaded with the address of the start of the interrupt-processing routine
    These two actions may each be a single micro-operation
    Because most processors provide multiple types and/or levels of interrupts, it may take one or more additional micro-operations to obtain the Save_Address and the Routine_Address before they can be transferred to the MAR and PC respectively
  Once this is done, the final step is to store the MBR, which contains the old value of the PC, into memory
  The processor is now ready to begin the next instruction cycle
Notes: At the completion of the execute cycle, a test is made to determine whether any
enabled interrupts have occurred. If so, the interrupt cycle occurs. The nature of this
cycle varies greatly from one machine to another. We present a very simple sequence
of events, as illustrated in Figure 16.7(Data Flow, Indirect Cycle). We have
t1: MBR  (PC)
t2: MAR  Save_Address
PC  Routine_Address
t3: Memory  (MBR)
In the first step, the contents of the PC are transferred to the MBR, so that
they can be saved for return from the interrupt. Then the MAR is loaded with
the address at which the contents of the PC are to be saved, and the PC is loaded
with the address of the start of the interrupt-processing routine. These two actions
may each be a single micro-operation. However, because most processors provide
multiple types and/or levels of interrupts, it may take one or more additional micro-
operations to obtain the Save_Address and the Routine_Address before they can
be transferred to the MAR and PC, respectively. In any case, once this is done, the
final step is to store the MBR, which contains the old value of the PC, into memory.
The processor is now ready to begin the next instruction cycle.

## Slide 9: Execute Cycle
Because of the variety of opcodes, there are a number of different sequences of micro-operations that can occur
Instruction decoding
  The control unit examines the opcode and generates a sequence of micro-operations based on the value of the opcode
A simplified add instruction:
  ADD R1, X (which adds the contents of the location X to register R1)
    In the first step the address portion of the IR is loaded into the MAR
    Then the referenced memory location is read
    Finally the contents of R1 and MBR are added by the ALU
    Additional micro-operations may be required to extract the register reference from the IR and perhaps to stage the ALU inputs or outputs in some intermediate registers
Notes: The fetch, indirect, and interrupt cycles are simple and predictable. Each involves
a small, fixed sequence of micro-operations and, in each case, the same micro-operations
are repeated each time around.
This is not true of the execute cycle. Because of the variety of opcodes, there
are a number of different sequences of micro-operations that can occur. The control
unit examines the opcode and generates a sequence of micro-operations based on
the value of the opcode. This is referred to as instruction decoding.
Let us consider several hypothetical examples.
First, consider an add instruction:
ADD R1, X
which adds the contents of the location X to register R1. The following sequence of
Micro-operations might occur:
t1: MAR  (IR(address))
t2: MBR  Memory
t3: R1  (R1) + (MBR)
We begin with the IR containing the ADD instruction. In the first step, the
address portion of the IR is loaded into the MAR. Then the referenced memory
location is read. Finally, the contents of R1 and MBR are added by the ALU. Again,
this is a simplified example. Additional micro-operations may be required to extract
the register reference from the IR and perhaps to stage the ALU inputs or outputs
in some intermediate registers.

## Slide 10: Figure 19.3 Flowchart for Instruction Cycle
Notes: We have seen that each phase of the instruction cycle can be decomposed into a
sequence of elementary micro-operations. In our example, there is one sequence
each for the fetch, indirect, and interrupt cycles, and, for the execute cycle, there is
one sequence of micro-operations for each opcode.
To complete the picture, we need to tie sequences of micro-operations
together, and this is done in Figure 19.3. We assume a new 2-bit register called the
instruction cycle code (ICC). The ICC designates the state of the processor in terms
of which portion of the cycle it is in:
00: Fetch
01: Indirect
10: Execute
11: Interrupt
At the end of each of the four cycles, the ICC is set appropriately. The indirect
cycle is always followed by the execute cycle. The interrupt cycle is always followed
by the fetch cycle (see Figure 16.3, (The Instruction Cycle ). For both the fetch and
execute cycles, the next cycle depends on the state of the system.
Thus, the flowchart of Figure 19.3 defines the complete sequence of micro-operations,
depending only on the instruction sequence and the interrupt pattern.
Of course, this is a simplified example. The flowchart for an actual processor would
be more complex. In any case, we have reached the point in our discussion in which
the operation of the processor is defined as the performance of a sequence of micro-
operations. We can now consider how the control unit causes this sequence to occur.

## Slide 11: Control Unit Functional Requirements
By reducing the operation of the processor to its most fundamental level we are able to define exactly what it is that the control unit must cause to happen
Three step process to lead to a characterization of the control unit:
  Define basic elements of processor
  Describe micro-operations processor performs
  Determine the functions that the control unit must perform to cause the micro-operations to be performed
The control unit performs two basic tasks:
  Sequencing
  Execution
Notes: As a result of our analysis in the preceding section, we have decomposed the behavior
or functioning of the processor into elementary operations, called micro-
operations. By reducing the operation of the processor to its most fundamental level, we are
able to define exactly what it is that the control unit must cause to happen. Thus, we
can define the functional requirements for the control unit: those functions that the
control unit must perform. A definition of these functional requirements is the basis
for the design and implementation of the control unit.
With the information at hand, the following three-step process leads to a characterization
of the control unit:
1. Define the basic elements of the processor.
2. Describe the micro-operations that the processor performs.
Determine the functions that the control unit must perform to cause the micro-operations
to be performed.
We have already performed steps 1 and 2. Let us summarize the results. First,
the basic functional elements of the processor are the following:
■ ALU
■ Registers
■ Internal data paths
■ External data paths
■ Control unit
Some thought should convince you that this is a complete list. The ALU is the
functional essence of the computer. Registers are used to store data internal to the
processor. Some registers contain status information needed to manage instruction
sequencing (e.g., a program status word). Others contain data that go to or come
from the ALU, memory, and I/O modules. Internal data paths are used to move
data between registers and between register and ALU. External data paths link
registers to memory and I/O modules, often by means of a system bus. The control
unit causes operations to happen within the processor.
The execution of a program consists of operations involving these processor
elements. As we have seen, these operations consist of a sequence of
micro-operations. Upon review of Section 19.1, the reader should see that all micro-operations
fall into one of the following categories:
■ Transfer data from one register to another.
■ Transfer data from a register to an external interface (e.g., system bus).
■ Transfer data from an external interface to a register.
■ Perform an arithmetic or logic operation, using registers for input and output.
All of the micro-operations needed to perform one instruction cycle, including all
of the micro-operations to execute every instruction in the instruction set, fall into
one of these categories.
We can now be somewhat more explicit about the way in which the control
unit functions. The control unit performs two basic tasks:
■ Sequencing: The control unit causes the processor to step through a series
of micro-operations in the proper sequence, based on the program being executed.
■ Execution: The control unit causes each micro-operation to be performed.
The preceding is a functional description of what the control unit does. The
key to how the control unit operates is the use of control signals.

## Slide 12: Basic elements
We have already performed steps 1 and 2. Let us summarize the results. First, the basic functional elements of the processor are the following:
■ ALU
■ Registers
■ Internal data paths
■ External data paths
■ Control unit

## Slide 13: Micro-operations and control unit
The execution of a program consists of operations involving these processor
elements. As we have seen, these operations consist of a sequence of micro-operations. Upon review of Section 20.1, the reader should see that all micro-operations fall into one of the following categories:
■ Transfer data from one register to another.
■ Transfer data from a register to an external interface (e.g., system bus).
■ Transfer data from an external interface to a register.
■ Perform an arithmetic or logic operation, using registers for input and output.
We can now be somewhat more explicit about the way in which the control
unit functions. The control unit performs two basic tasks:
■ Sequencing: The control unit causes the processor to step through a series
of micro-operations in the proper sequence, based on the program being executed.
■ Execution: The control unit causes each micro-operation to be performed.

## Slide 14: Figure 19.4 Block Diagram of the Control Unit
Notes: We have defined the elements that make up the processor (ALU, registers, data
paths) and the micro-operations that are performed. For the control unit to perform
its function, it must have inputs that allow it to determine the state of the system and
outputs that allow it to control the behavior of the system. These are the external
specifications of the control unit. Internally, the control unit must have the logic
required to perform its sequencing and execution functions. We defer a discussion
of the internal operation of the control unit to Section 19.3 and Chapter 19.4. The
remainder of this section is concerned with the interaction between the control unit
and the other elements of the processor.
Figure 19.4 is a general model of the control unit, showing all of its inputs and
outputs. The inputs are:
■ Clock: This is how the control unit “keeps time.” The control unit causes one
micro-operation (or a set of simultaneous micro-operations) to be performed
for each clock pulse. This is sometimes referred to as the processor cycle time,
or the clock cycle time.
■ Instruction register: The opcode and addressing mode of the current instruction
are used to determine which micro-operations to perform during the execute cycle.
■ Flags: These are needed by the control unit to determine the status of the
processor and the outcome of previous ALU operations. For example, for the
Increment-and-skip-if-zero (ISZ) instruction, the control unit will increment
the PC if the zero flag is set.
■ Control signals from control bus: The control bus portion of the system bus
provides signals to the control unit.
The outputs are as follows:
■ Control signals within the processor: These are two types: those that cause
data to be moved from one register to another, and those that activate specific
ALU functions.
■ Control signals to control bus: These are also of two types: control signals to
memory, and control signals to the I/O modules.
Three types of control signals are used: those that activate an ALU function;
those that activate a data path; and those that are signals on the external system bus
or other external interface. All of these signals are ultimately applied directly as
binary inputs to individual logic gates.
Let us consider again the fetch cycle to see how the control unit maintains
control. The control unit keeps track of where it is in the instruction cycle. At a
given point, it knows that the fetch cycle is to be performed next. The first step is to
transfer the contents of the PC to the MAR. The control unit does this by activating
the control signal that opens the gates between the bits of the PC and the bits of
the MAR. The next step is to read a word from memory into the MBR and increment
the PC. The control unit does this by sending the following control signals
simultaneously:
■ A control signal that opens gates, allowing the contents of the MAR onto the
address bus;
■ A memory read control signal on the control bus;
■ A control signal that opens the gates, allowing the contents of the data bus to
be stored in the MBR;
■ Control signals to logic that add 1 to the contents of the PC and store the
result back to the PC.
Following this, the control unit sends a control signal that opens gates between the
MBR and the IR.
This completes the fetch cycle except for one thing: The control unit must
decide whether to perform an indirect cycle or an execute cycle next. To decide this,
it examines the IR to see if an indirect memory reference is made.
The indirect and interrupt cycles work similarly. For the execute cycle, the
control unit begins by examining the opcode and, on the basis of that, decides which
sequence of micro-operations to perform for the execute cycle.

## Slide 15: Figure 19.5 Data Paths and Control Signals
Notes: To illustrate the functioning of the control unit, let us examine a simple example.
Figure 19.5 illustrates the example. This is a simple processor with a single accumulator
(AC). The data paths between elements are indicated. The control paths
for signals emanating from the control unit are not shown, but the terminations of
control signals are labeled Ci and indicated by a circle. The control unit receives
inputs from the clock, the IR, and flags. With each clock cycle, the control unit
reads all of its inputs and emits a set of control signals. Control signals go to three
separate destinations:
■ Data paths: The control unit controls the internal flow of data. For example, on
instruction fetch, the contents of the memory buffer register are transferred to
the IR. For each path to be controlled, there is a switch (indicated by a circle in
the figure). A control signal from the control unit temporarily opens the gate
to let data pass.
■ ALU: The control unit controls the operation of the ALU by a set of control
signals. These signals activate various logic circuits and gates within the ALU.
■ System bus: The control unit sends control signals out onto the control lines of
the system bus (e.g., memory READ).

## Slide 16
To illustrate the functioning of the control unit, let us examine a simple example. Figure 20.5 illustrates the example. This is a simple processor with a single accumulator (AC). The data paths between elements are indicated. The control paths for signals emanating from the control unit are not shown, but the terminations of control signals are labeled Ci and indicated by a circle
Notes: To illustrate the functioning of the control unit, let us examine a simple example.
Figure 20.5 illustrates the example. This is a simple processor with a single accumulator
(AC). The data paths between elements are indicated. The control paths
for signals emanating from the control unit are not shown, but the terminations of
control signals are labeled Ci and indicated by a circle. The control unit receives
inputs from the clock, the IR, and flags. With each clock cycle, the control unit
reads all of its inputs and emits a set of control signals. Control signals go to three
separate destinations:
■ Data paths: The control unit controls the internal flow of data. For example, on
instruction fetch, the contents of the memory buffer register are transferred to
the IR. For each path to be controlled, there is a switch (indicated by a circle in
the figure). A control signal from the control unit temporarily opens the gate
to let data pass.
■ ALU: The control unit controls the operation of the ALU by a set of control
signals. These signals activate various logic circuits and gates within the ALU.
■ System bus: The control unit sends control signals out onto the control lines of
the system bus (e.g., memory READ).

## Slide 17
With each clock cycle, the control unit reads all of its inputs and emits a set of control signals. Control signals go to three separate destinations:
■ Data paths: The control unit controls the internal flow of data. For example, on instruction fetch, the contents of the memory buffer register are transferred to the IR. For each path to be controlled, there is a switch (indicated by a circle in the figure). A control signal from the control unit temporarily opens the gate to let data pass.
■ ALU: The control unit controls the operation of the ALU by a set of control signals. These signals activate various logic circuits and gates within the ALU.
■ System bus: The control unit sends control signals out onto the control lines of the system bus (e.g., memory READ).
Notes: To illustrate the functioning of the control unit, let us examine a simple example.
Figure 20.5 illustrates the example. This is a simple processor with a single accumulator
(AC). The data paths between elements are indicated. The control paths
for signals emanating from the control unit are not shown, but the terminations of
control signals are labeled Ci and indicated by a circle. The control unit receives
inputs from the clock, the IR, and flags. With each clock cycle, the control unit
reads all of its inputs and emits a set of control signals. Control signals go to three
separate destinations:
■ Data paths: The control unit controls the internal flow of data. For example, on
instruction fetch, the contents of the memory buffer register are transferred to
the IR. For each path to be controlled, there is a switch (indicated by a circle in
the figure). A control signal from the control unit temporarily opens the gate
to let data pass.
■ ALU: The control unit controls the operation of the ALU by a set of control
signals. These signals activate various logic circuits and gates within the ALU.
■ System bus: The control unit sends control signals out onto the control lines of
the system bus (e.g., memory READ).

## Slide 18: Table 19.1 Micro-operations and Control Signals
 | Micro-operations | Active Control Signals
Fetch: | t1: MAR ← (PC) | C2
 | t2: MBR ← Memory PC ← (PC) + 1 | C5, CR
 | t3: IR ← (MBR) | C4
Indirect: | t1: MAR ← (IR(Address)) | C8
 | t2: MBR ← Memory | C5, CR
 | t3: IR(Address) ← (MBR(Address)) | C4
Interrupt: | t1: MBR ← (PC) | C1
 | t2 : MAR ← Save-address PC ← Routine-address | 
 | t3: Memory ← (MBR) | C12, CW
CR = Read control signal to system bus.
CW = Write control signal to system bus.
(Table can be found on page 681in the textbook.)
Notes: The control unit must maintain knowledge of where it is in the instruction
cycle. Using this knowledge, and by reading all of its inputs, the control unit emits
a sequence of control signals that causes micro-operations to occur. It uses the
clock pulses to time the sequence of events, allowing time between events for signal
levels to stabilize. Table 19.1 indicates the control signals that are needed for
some of the micro-operation sequences described earlier. For simplicity, the data
and control paths for incrementing the PC and for loading the fixed addresses into
the PC and MAR are not shown.
It is worth pondering the minimal nature of the control unit. The control unit
is the engine that runs the entire computer. It does this based only on knowing the
instructions to be executed and the nature of the results of arithmetic and logical
operations (e.g., positive, overflow, etc.). It never gets to see the data being processed
or the actual results produced. And it controls everything with a few control
signals to points within the processor and a few control signals to the system bus.

## Slide 19
Using an internal processor bus, Figure 20.5 can be rearranged as shown in Figure 20.6. A single internal bus connects the ALU and all processor registers. Gates and control signals are provided for movement of data onto and off the bus from each register. Additional control signals control data transfer to and from the system (external) bus and the operation of the ALU.
Two new registers, labeled Y and Z, have been added to the organization.
These are needed for the proper operation of the ALU. When an operation involving two operands is performed, one can be obtained from the internal bus, but the other must be obtained from another source. The AC could be used for this purpose, but this limits the flexibility of the system and would not work with a processor with multiple general-purpose registers. Register Y provides temporary storage for the other input. The ALU is a combinatorial circuit (see Chapter 11) with no internal storage. Thus, when control signals activate an ALU function, the input to the ALU is transformed to the output. Therefore, the output of the ALU cannot be directly connected to the bus, because this output would feed back to the input. Register Z provides temporary output storage.
Notes: Figure 20.5 indicates the use of a variety of data paths. The complexity of this type of
organization should be clear. More typically, some sort of internal bus arrangement,
as was suggested in Figure 14.2 (Internal Structure of the CPU ), will be used.
Using an internal processor bus, Figure 20.5 can be rearranged as shown in
Figure 20.6. A single internal bus connects the ALU and all processor registers.
Gates and control signals are provided for movement of data onto and off the bus
from each register. Additional control signals control data transfer to and from the
system (external) bus and the operation of the ALU.
Two new registers, labeled Y and Z, have been added to the organization.
These are needed for the proper operation of the ALU. When an operation involving
two operands is performed, one can be obtained from the internal bus, but the
other must be obtained from another source. The AC could be used for this purpose,
but this limits the flexibility of the system and would not work with a processor
with multiple general-purpose registers. Register Y provides temporary storage
for the other input. The ALU is a combinatorial circuit (see Chapter 11) with no
internal storage. Thus, when control signals activate an ALU function, the input to
the ALU is transformed to the output. Therefore, the output of the ALU cannot
be directly connected to the bus, because this output would feed back to the input.
Register Z provides temporary output storage.

## Slide 20: Figure 19.7 Intel 8085 CPU Block Diagram
Notes: To illustrate some of the concepts introduced thus far in this chapter, let us consider
the Intel 8085. Its organization is shown in Figure 19.7. Several key components that
may not be self-explanatory are:
■ Incrementer/decrementer address latch: Logic that can add 1 to or subtract 1
from the contents of the stack pointer or program counter. This saves time by
avoiding the use of the ALU for this purpose.
■ Interrupt control: This module handles multiple levels of interrupt signals.
■ Serial I/O control: This module interfaces to devices that communicate 1 bit
at a time.

## Slide 21: Table 19.2 Intel 8085 External Signals (page 1 of 2)
Address and Data Signals High Address (A15–A8) The high-order 8 bits of a 16-bit address. Address/Data (AD7–AD0) The lower-order 8 bits of a 16-bit address or 8 bits of data. This multiplexing saves on pins. Serial Input Data (SID) A single-bit input to accommodate devices that transmit serially (one bit at a time). Serial Output Data (SOD) A single-bit output to accommodate devices that receive serially. Timing and Control Signals CLK (OUT) The system clock. The CLK signal goes to peripheral chips and synchronizes their timing. X1, X2 These signals come from an external crystal or other device to drive the internal clock generator. Address Latch Enabled (ALE) Occurs during the first clock state of a machine cycle and causes peripheral chips to store the address lines. This allows the address module (e.g., memory, I/O) to recognize that it is being addressed. Status (S0, S1) Control signals used to indicate whether a read or write operation is taking place. IO/M Used to enable either I/O or memory modules for read and write operations. Read Control (RD) Indicates that the selected memory or I/O module is to be read and that the data bus is available for data transfer. Write Control (WR) Indicates that data on the data bus is to be written into the selected memory or I/O location.
(Table can be found on page 684 in the textbook.)
Notes: Table 19.2 describes the external signals into and out of the 8085. These are
linked to the external system bus.

## Slide 22: Table 19.2 Intel 8085 External Signals (page 2 of 2)
Memory and I/O Initiated Symbols Hold Requests the CPU to relinquish control and use of the external system bus. The CPU will complete execution of the instruction presently in the IR and then enter a hold state, during which no signals are inserted by the CPU to the control, address, or data buses. During the hold state, the bus may be used for DMA operations. Hold Acknowledge (HOLDA) This control unit output signal acknowledges the HOLD signal and indicates that the bus is now available. READY Used to synchronize the CPU with slower memory or I/O devices. When an addressed device asserts READY, the CPU may proceed with an input (DBIN) or output (WR) operation. Otherwise, the CPU enters a wait state until the device is ready. Interrupt-Related Signals TRAP Restart Interrupts (RST 7.5, 6.5, 5.5) Interrupt Request (INTR) These five lines are used by an external device to interrupt the CPU. The CPU will not honor the request if it is in the hold state or if the interrupt is disabled. An interrupt is honored only at the completion of an instruction. The interrupts are in descending order of priority. Interrupt Acknowledge Acknowledges an interrupt. CPU Initialization RESET IN Causes the contents of the PC to be set to zero. The CPU resumes execution at location zero. RESET OUT Acknowledges that the CPU has been reset. The signal can be used to reset the rest of the system. Voltage and Ground VCC +5-volt power supply VSS Electrical ground
Notes: Table 19.2, continued.

## Slide 23: Figure 19.8 Intel 8085 Pin Configuration
Notes: These signals are the interface between the 8085
processor and the rest of the system (Figure 19.8).
The control unit is identified as having two components labeled (1) instruction
decoder and machine cycle encoding and (2) timing and control. A discussion
of the first component is deferred until the next section. The essence of the control
unit is the timing and control module. This module includes a clock and accepts as
inputs the current instruction and some external control signals. Its output consists
of control signals to the other components of the processor plus control signals to
the external system bus.
The timing of processor operations is synchronized by the clock and controlled
by the control unit with control signals. Each instruction cycle is divided into from
one to five machine cycles; each machine cycle is in turn divided into from three to
five states. Each state lasts one clock cycle. During a state, the processor performs
one or a set of simultaneous micro-operations as determined by the control signals.
The number of machine cycles is fixed for a given instruction but varies
from one instruction to another. Machine cycles are defined to be equivalent to
bus accesses. Thus, the number of machine cycles for an instruction depends on
the number of times the processor must communicate with external devices. For
example, if an instruction consists of two 8-bit portions, then two machine cycles are
required to fetch the instruction. If that instruction involves a 1-byte memory or I/O
operation, then a third machine cycle is required for execution.

## Slide 24: Figure 19.9 Timing Diagram for Intel 8085 OUT Instruction
Notes: Figure 19.9 gives an example of 8085 timing, showing the value of external
control signals. Of course, at the same time, the control unit generates internal control
signals that control internal data transfers. The diagram shows the instruction
cycle for an OUT instruction. Three machine cycles (M1 , M2 , M3 ) are needed. During
the first, the OUT instruction is fetched. The second machine cycle fetches the
second half of the instruction, which contains the number of the I/O device selected
for output. During the third cycle, the contents of the AC are written out to the
selected device over the data bus.
The Address Latch Enabled (Ale ) pulse signals the start of each machine
cycle from the control unit. The Ale pulse alerts external circuits. During timing
state T1 of machine cycle M1 , the control unit sets the IO/M signal to indicate that
this is a memory operation. Also, the control unit causes the contents of the PC
to be placed on the address bus (A15 through A8 ) and the address/data bus (AD7
through AD0 ). With the falling edge of the Ale pulse, the other modules on the
bus store the address.
During timing state T2 , the addressed memory module places the contents of the
addressed memory location on the address/data bus. The control unit sets the Read
Control (RD) signal to indicate a read, but it waits until T3 to copy the data from the
bus. This gives the memory module time to put the data on the bus and for the signal
levels to stabilize. The final state, T4 , is a bus idle state during which the processor
decodes the instruction. The remaining machine cycles proceed in a similar fashion.

## Slide 25: Control Unit Implementation
A wide variety of techniques have been used for control unit implementation
Most of these fall into two categories:
  Hardwired implementation
      The control unit is essentially a state machine circuit
      Its input logic signals are transformed into a set of output logic signals, which are the control signals
  Microprogrammed implementation
Notes: We have discussed the control unit in terms of its inputs, output, and functions. We
now turn to the topic of control unit implementation. A wide variety of techniques
have been used. Most of these fall into one of two categories:
■ Hardwired implementation
■ Microprogrammed implementation
In a hardwired implementation, the control unit is essentially a state machine
circuit. Its input logic signals are transformed into a set of output logic signals, which
are the control signals. This approach is examined in this section. Microprogrammed
implementation is the subject of Section 19.4.

## Slide 26: Table 19.3 A Decoder With 4 Inputs and 16 Outputs
I1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
I2 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
I3 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
I4 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
O1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
O2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
O3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
O4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
O5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
O6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
O7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
O8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O10 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O11 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O12 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O13 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O14 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O15 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
O16 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
(Table can be found on page 687in the textbook.)
Notes: Figure 19.4 depicts the control unit as we have so far discussed it. The key inputs are
the IR, the clock, flags, and control bus signals. In the case of the flags and control
bus signals, each individual bit typically has some meaning (e.g., overflow). The other
two inputs, however, are not directly useful to the control unit.
First consider the IR. The control unit makes use of the opcode and will perform
different actions (issue a different combination of control signals) for different
instructions. To simplify the control unit logic, there should be a unique logic input for
each opcode. This function can be performed by a decoder , which takes an encoded
input and produces a single output. In general, a decoder will have n binary inputs and
2n binary outputs. Each of the 2n different input patterns will activate a single unique
output. Table 19.3 is an example for n = 4. The decoder for a control unit will typically
have to be more complex than that, to account for variable-length opcodes. An
example of the digital logic used to implement a decoder is presented in Chapter 12.

## Slide 27: Figure 19.10 Control Unit with Decoded Inputs
Notes: The clock portion of the control unit issues a repetitive sequence of pulses.
This is useful for measuring the duration of micro-operations. Essentially, the period
of the clock pulses must be long enough to allow the propagation of signals along
data paths and through processor circuitry. However, as we have seen, the control
unit emits different control signals at different time units within a single instruction
cycle. Thus, we would like a counter as input to the control unit, with a different
control signal being used for T1 ,T2 , and so forth. At the end of an instruction cycle,
the control unit must feed back to the counter to reinitialize it at T1 .
With these two refinements, the control unit can be depicted as in Figure 19.10.

## Slide 28: Microprogrammed Control
The term microprogrammed was first coined by M.V. Wilkes in the early 1950’s
Wilkes proposed an approach to control unit design that was organized and systematic and avoided the complexities of a hardwired implementation
The idea intrigued many researchers but appeared unworkable because it would require a fast, relatively inexpensive control memory
In April of 1964 IBM’s System/360 was announced and all but the largest models were microprogrammed
Microprogramming became a popular technique for implementing the control unit of CISC processors
In recent years, microprogramming has become less used but remains a tool available to computer designers
Notes: The term microprogram was first coined by M. V. Wilkes in the early 1950s [WILK51].
Wilkes proposed an approach to control unit design that was organized and systematic
and avoided the complexities of a hardwired implementation. The idea intrigued
many researchers but appeared unworkable because it would require a fast, relatively
inexpensive control memory.
The state of the microprogramming art was reviewed by Datamation in its
February 1964 issue. No microprogrammed system was in wide use at that time,
and one of the papers [HILL64] summarized the then-popular view that the future
of microprogramming “is somewhat cloudy. None of the major manufacturers has
evidenced interest in the technique, although presumably all have examined it.”
This situation changed dramatically within a very few months. IBM’s System/
360 was announced in April, and all but the largest models were microprogrammed.
Although the 360 series predated the availability of semiconductor
ROM, the advantages of microprogramming were compelling enough for IBM
to make this move. Microprogramming became a popular technique for implementing
the control unit of CISC processors. In recent years, microprogramming
has become less used but remains a tool available to computer designers.
For example, as we have seen on the Pentium 4, machine instructions are converted
into a RISC-like format, most of which are executed without the use
of microprogramming. However, some of the instructions are executed using
microprogramming.

## Slide 29: Table 19.4 Machine Instruction Set for Wilkes Example
Order | Effect of Order
A n | C(Acc) + C(n) to Acc1
S n | C(Acc) – C(n) to Acc1
H n | C(n) to Acc2
V n | C(Acc2) × C(n) to Acc, where C(n) ≥ 0
T n | C(Acc1) to n, 0 to Acc
U n | C(Acc1) to n
R n | C(Acc) × 2(n+1) to Acc
L n | C(Acc) × 2n+1 to Acc
G n | IF C(Acc) < 0, transfer control to n; if C(Acc) ≥ 0, ignore (i.e., proceed serially)
I n | Read next character on input mechanism into n
O n | Send C(n) to output mechanism
Notation: Acc = accumulator
Acc1 = most significant half of accumulator
Acc2 = least significant half of accumulator
n = storage location n
C(X) = contents of X(X = register or storage location)
Notes: The control unit seems a reasonably simple device. Nevertheless, to implement a control
unit as an interconnection of basic logic elements is no easy task. The design must
include logic for sequencing through micro-operations, for executing micro-operations,
for interpreting opcodes, and for making decisions based on ALU flags. It is difficult to
design and test such a piece of hardware. Furthermore, the design is relatively inflexible.
For example, it is difficult to change the design if one wishes to add a new machine
instruction.
An alternative, which has been used in many CISC processors, is to implement
a microprogrammed control unit .
Consider Table 19.4. In addition to the use of control signals, each micro-operation
is described in symbolic notation. This notation looks suspiciously like
a programming language. In fact it is a language, known as a microprogramming
language . Each line describes a set of micro-operations occurring at one time and
is known as a microinstruction. A sequence of instructions is known as a microprogram ,
or firmware . This latter term reflects the fact that a microprogram is midway
between hardware and software. It is easier to design in firmware than hardware,
but it is more difficult to write a firmware program than a software program.

## Slide 30: Figure 19.12 Typical Microinstruction Formats
Notes: How can we use the concept of microprogramming to implement a control
unit? Consider that for each micro-operation, all that the control unit is allowed
to do is generate a set of control signals. Thus, for any micro-operation, each control
line emanating from the control unit is either on or off. This condition can, of
course, be represented by a binary digit for each control line. So we could construct
a control word in which each bit represents one control line. Then each micro-operation
would be represented by a different pattern of 1s and 0s in the control word.
Suppose we string together a sequence of control words to represent the
sequence of micro-operations performed by the control unit. Next, we must recognize
that the sequence of micro-operations is not fixed. Sometimes we have an
indirect cycle; sometimes we do not. So let us put our control words in a memory,
with each word having a unique address. Now add an address field to each control
word, indicating the location of the next control word to be executed if a certain
condition is true (e.g., the indirect bit in a memory-reference instruction is 1). Also,
add a few bits to specify the condition.
The result is known as a horizontal microinstruction, an example of which
is shown in Figure 19.12a. The format of the microinstruction or control word is as
follows. There is one bit for each internal processor control line and one bit for each
system bus control line. There is a condition field indicating the condition under
which there should be a branch, and there is a field with the address of the microinstruction
to be executed next when a branch is taken. Such a microinstruction is
interpreted as follows:
1. To execute this microinstruction, turn on all the control lines indicated by a 1
bit; leave off all control lines indicated by a 0 bit. The resulting control signals
will cause one or more micro-operations to be performed.
2. If the condition indicated by the condition bits is false, execute the next microinstruction
in sequence.
3. If the condition indicated by the condition bits is true, the next microinstruction
to be executed is indicated in the address field.

## Slide 31: Figure 19.13 Organization of Control Memory
Notes: Figure 19.13 shows how these control words or microinstructions could be
arranged in a control memory . The microinstructions in each routine are to be executed
sequentially. Each routine ends with a branch or jump instruction indicating
where to go next. There is a special execute cycle routine whose only purpose is to
signify that one of the machine instruction routines (AND, ADD, and so on) is to
be executed next, depending on the current opcode.
The control memory of Figure 19.13 is a concise description of the complete
operation of the control unit. It defines the sequence of micro-operations to be
performed during each cycle (fetch, indirect, execute, interrupt), and it specifies the
sequencing of these cycles. If nothing else, this notation would be a useful device
for documenting the functioning of a control unit for a particular computer. But it is
more than that. It is also a way of implementing the control unit.

## Slide 32: Figure 19.14 Control Unit Microarchitecture
Notes: The control memory of Figure 19.13 contains a program that describes the behavior
of the control unit. It follows that we could implement the control unit by simply
executing that program.
Figure 19.14 shows the key elements of such an implementation. The set of
microinstructions is stored in the control memory . The control address register contains
the address of the next microinstruction to be read. When a microinstruction is
read from the control memory, it is transferred to a control buffer register. The lefthand
portion of that register (see Figure 19.12a) connects to the control lines emanating
from the control unit. Thus, reading a microinstruction from the control memory
is the same as executing that microinstruction. The third element shown in the figure is
a sequencing unit that loads the control address register and issues a read command.

## Slide 33: Figure 19.15 Functioning of Microprogrammed Control Unit
Notes: Let us examine this structure in greater detail, as depicted in Figure 19.15. Comparing
this with Figure 19.14, we see that the control unit still has the same inputs (IR,
ALU flags, clock) and outputs (control signals). The control unit functions as follows:
1. To execute an instruction, the sequencing logic unit issues a READ command
to the control memory.
2. The word whose address is specified in the control address register is read into
the control buffer register.
3. The content of the control buffer register generates control signals and
next-address information for the sequencing logic unit.
4. The sequencing logic unit loads a new address into the control address register
based on the next-address information from the control buffer register and the
ALU flags.
All this happens during one clock pulse.
The last step just listed needs elaboration. At the conclusion of each microinstruction,
the sequencing logic unit loads a new address into the control address
register. Depending on the value of the ALU flags and the control buffer register,
one of three decisions is made:
■ Get the next instruction: Add 1 to the control address register.
■ Jump to a new routine based on a jump microinstruction: Load the address
field of the control buffer register into the control address register.
■ Jump to a machine instruction routine: Load the control address register
based on the opcode in the IR.
Figure 19.15 shows two modules labeled decoder . The upper decoder translates
the opcode of the IR into a control memory address. The lower decoder is
not used for horizontal microinstructions but is used for vertical microinstructions
(Figure 19.12b). As was mentioned, in a horizontal microinstruction every bit in the
control field attaches to a control line. In a vertical microinstruction, a code is used
for each action to be performed [e.g., MAR  (PC)], and the decoder translates
this code into individual control signals. The advantage of vertical microinstructions
is that they are more compact (fewer bits) than horizontal microinstructions,
at the expense of a small additional amount of logic and time delay.

## Slide 34: Figure 19.16 Wilkes’s Microprogrammed Control Unit
Notes: As was mentioned, Wilkes first proposed the use of a microprogrammed control unit
in 1951 [WILK51]. This proposal was subsequently elaborated into a more detailed
design [WILK53]. It is instructive to examine this seminal proposal.
The configuration proposed by Wilkes is depicted in Figure 19.16. The heart of the
system is a matrix partially filled with diodes. During a machine cycle, one row of the
matrix is activated with a pulse. This generates signals at those points where a diode is
present (indicated by a dot in the diagram). The first part of the row generates the control
signals that control the operation of the processor. The second part generates the
address of the row to be pulsed in the next machine cycle. Thus, each row of the matrix
is one microinstruction, and the layout of the matrix is the control memory.
At the beginning of the cycle, the address of the row to be pulsed is contained
in Register I. This address is the input to the decoder, which, when activated by
a clock pulse, activates one row of the matrix. Depending on the control signals,
either the opcode in the instruction register or the second part of the pulsed row is
passed into Register II during the cycle. Register II is then gated to Register I by
a clock pulse. Alternating clock pulses are used to activate a row of the matrix and
to transfer from Register II to Register I. The two-register arrangement is needed
because the decoder is simply a combinatorial circuit; with only one register, the
output would become the input during a cycle, causing an unstable condition.
This scheme is very similar to the horizontal microprogramming approach
described earlier (Figure 19.12a). The main difference is this: In the previous description,
the control address register could be incremented by one to get the next
address. In the Wilkes scheme, the next address is contained in the microinstruction.
To permit branching, a row must contain two address parts, controlled by a
conditional signal (e.g., flag), as shown in the figure.
Having proposed this scheme, Wilkes provides an example of its use to implement
the control unit of a simple machine. This example, the first known design of a
microprogrammed processor, is worth repeating here because it illustrates many of
the contemporary principles of microprogramming.

## Slide 35: Table 19.5 Microinstructions for Wilkes Example (Page 1 of 2)
Notations: A, B, C, . . . stand for the various registers in the arithmetical and control register units. C to D indicates
that the switching circuits connect the output of register C to the input register D; (D + A) to C indicates that the
output register of A is connected to the one input of the adding unit (the output of D is permanently connected to
the other input), and the output of the adder to register C. A numerical symbol n in quotes (e.g., “n”) stands for the
source whose output is the number n in units of the least significant digit.
 |  | Arithmetical Unit | Control Register Unit | Conditional Flip-Flop |  | Next Microinstruction | 
 |  |  |  | Set | Use | 0 | 1
 | 0 |  | F to G and E |  |  | 1 | 
 | 1 |  | (G to “1”) to F |  |  | 2 | 
 | 2 |  | Store to G |  |  | 3 | 
 | 3 |  | G to E |  |  | 4 | 
 | 4 |  | E to decoder |  |  | – | 
A | 5 | C to D |  |  |  | 16 | 
S | 6 | C to D |  |  |  | 17 | 
H | 7 | Store to B |  |  |  | 0 | 
V | 8 | Store to A |  |  |  | 27 | 
T | 9 | C to Store |  |  |  | 25 | 
U | 10 | C to Store |  |  |  | 0 | 
R | 11 | B to D | E to G |  |  | 19 | 
L | 12 | C to D | E to G |  |  | 22 | 
G | 13 |  | E to G | (1)C5 |  | 18 | 
I | 14 | Input to Store |  |  |  | 0 | 
O | 15 | Store to Output |  |  |  | 0 | 
 | 16 | (D + Store) to C |  |  |  | 0 | 
 | 17 | (D – Store) to C |  |  |  | 0 | 
 | 18 |  |  |  | 1 | 0 | 1
 | 19 | D to B (R)* | (G – 1) to E |  |  | 20 | 
 | 20 | C to D |  | (1)E5 |  | 21 | 
(Table can be found on pages 697-698 in the textbook.)
Notes: Table 19.5 is the complete set of microinstructions, expressed in symbolic form, that implements
the control unit. Thus, a total of 38 microinstructions is all that is required to define
the system completely.
The first full column gives the address (row number) of each microinstruction.
Those addresses corresponding to opcodes are labeled. Thus, when the opcode for
the add instruction (A) is encountered, the microinstruction at location 5 is executed.
Columns 2 and 3 express the actions to be taken by the ALU and control
unit, respectively. Each symbolic expression must be translated into a set of control
signals (microinstruction bits). Columns 4 and 5 have to do with the setting and
use of the two flags (flip-flops). Column 4 specifies the signal that sets the flag. For
example, (1)Cs means that flag number 1 is set by the sign bit of the number in register
C. If column 5 contains a flag identifier, then columns 6 and 7 contain the two
alternative microinstruction addresses to be used. Otherwise, column 6 specifies the
address of the next microinstruction to be fetched.
Instructions 0 through 4 constitute the fetch cycle. Microinstruction 4 presents
the opcode to a decoder, which generates the address of a microinstruction corresponding
to the machine instruction to be fetched. The reader should be able to
deduce the complete functioning of the control unit from a careful study of Table 19.5.

## Slide 36: Table 19.5 Microinstructions for Wilkes Example (Page 2 of 2)
 |  | Arithmetical Unit | Control Register Unit | Conditional Flip-Flop |  | Next Microinstruction | 
 |  |  |  | Set | Use | 0 | 1
 | 21 | D to C (R) |  |  | 1 | 11 | 0
 | 22 | D to C (L)† | (G - 1) to E |  |  | 23 | 
 | 23 | B to D |  | (1)E5 |  | 24 | 
 | 24 | D to B (L) |  |  | 1 | 12 | 0
 | 25 | “0” to B |  |  |  | 26 | 
A | 26 | B to C |  |  |  | 0 | 
S | 27 | “0” to C | “18” to E |  |  | 28 | 
H | 28 | B to D | E to G | (1)B1 |  | 29 | 
V | 29 | D to B (R) | (G - “1”) to E |  |  | 30 | 
T | 30 | C to D (R) |  | (2)E5 | 1 | 31 | 32
U | 31 | D to C |  |  | 2 | 28 | 33
R | 32 | (D + A) to C |  |  | 2 | 28 | 33
L | 33 | B to D |  | (1)B1 |  | 34 | 
G | 34 | D to B (R) |  |  |  | 35 | 
I | 35 | C to D (R) |  |  | 1 | 36 | 37
O | 36 | D to C |  |  |  | 0 | 
 | 37 | (D - A) to C |  |  |  | 0 | 
* Right shift. The switching circuits in the arithmetic unit are arranged so that the least significant digit of the
register C is placed in the most significant place of register B during right shift micro-operations, and the most
significant digit of register C (sign digit) is repeated (thus making the correction for negative numbers).
† Left shift. The switching circuits are similarly arranged to pass the most significant digit of register B to the
least significant place of register C during left shift micro-operations.
(Table can be found on pages 697-698 in the textbook.)
Notes: The principal advantage of the use of microprogramming to implement a control
unit is that it simplifies the design of the control unit. Thus, it is both cheaper and
less error prone to implement. A hardwired control unit must contain complex logic
for sequencing through the many micro-operations of the instruction cycle. On the
other hand, the decoders and sequencing logic unit of a microprogrammed control
unit are very simple pieces of logic.
The principal disadvantage of a microprogrammed unit is that it will be somewhat
slower than a hardwired unit of comparable technology. Despite this, microprogramming
is the dominant technique for implementing control units in pure
CISC architectures, due to its ease of implementation. RISC processors, with their
simpler instruction format, typically use hardwired control units.

## Slide 37: Summary
Chapter 19
Micro-operations
  The fetch cycle
  The indirect cycle
  The interrupt cycle
  The execute cycle
  The instruction cycle
  Microprogramed control
  Microinstructions
  Microprogrammed control unit
  Wilkes control
  Advantages and disadvantages
Control Unit Operation and Microprogrammed Control
Control of the processor
  Functional requirements
  Control signals
  Internal processor organization
  The Intel 8085
Hardwired implementation
  Control unit inputs
  Control unit logic
Notes: Chapter 19 summary.